##### ANEXOS

Tabela A2.1- Comparação das características metodológicas e dos resultados de três inventários portugueses de resíduos

|  | Tecninvest | Scoreco | INE | PESGRI 99 |
| --- | --- | --- | --- | --- |
| Ano a que se refere | 1996 (revisão do inventário de 1994) | 1996 | 1995 e 1997 | 1998 |
| Objectivos | Caracterizar a situação da produção de resíduos perigosos e analisar as opções de gestão, nomeadamente a médio prazo | Esclarecer a Comissão de Avaliação do Impacte Ambiental (CAIA) sobre a natureza e quantidade de resíduos | Recolher informação relativa à situação dos resíduos resultantes das actividades industriais em Portugal, iniciando um processo de observação estatística regular, sobre as quantidades de resíduos industriais e operações de gestão (eliminação/ valorização) a que são submetidos | Fundamentar sugestões e recomendações para a tomada de decisões no domínio dos resíduos industriais, tendo como base os quantitativos obtidos através dos procedimentos legais em curso |
| Recolha e tratamento de informação | Recolha directa junto dos maiores produtores Correcção nos sectores industriais de menor significado, com base nos níveis de produção, através das estatísticas de produção mais recentes (Índices de Produção Industrial, Banco de Portugal, Relatório Anual de 1995). Informação obtida dos maiores produtores complementada com a dos mapas de registo de resíduos dos estabelecimentos industriais (Instituto de Resíduos) Contactos directos com os responsáveis pelos principais sistemas de gestão de resíduos, então em funcionamento ou a implementar a curto prazo (Scoreco, Autovila, Quimitécnica, ECTRI, ETAR, Instituto da água, DRARN-Norte) | Recolha de informação realizada pelos serviços comerciais da SCORECO, desde o Outono de 1995. Os quantitativos de óleos usados foram estimados com base em dados estatísticos europeus de produção e consumo de óleos minerais. A quantidade de embalagens contaminadas resulta de inquéritos sobre os modos de acondicionamento mais usados pelos industriais, bem como sobre estatísticas de vendas de produtos químicos e afins na Europa (são os únicos números da SCORECO que não correspondem a um recenseamento minucioso dos produtores, antes se apoiam na aplicação de índices de actividade e parâmetros económicos) | A base de amostragem considerou todas as empresas classificadas nas secções C, D, E e F da CAE Rev. 2 com 20 e/ou mais pessoas ao serviço. A recolha de dados fez-se numa primeira fase por via postal: quando as diligências por esta via se revelaram esgotadas, recorreu-se a entrevistadores para recolha directa da informação junto das empresas. Como metodologia de tratamento de não respostas, foi adoptado um processo equivalente a imputar às não respostas a média dos resultados obtidos nas respostas do estrato a que pertencem. | Os quantitativos de resíduos perigosos apresentados baseiam-se nos mapas de resíduos que cada produtor de resíduos industriais deve preencher, identificando os resíduos de acordo com o CER, e remeter anualmente à DRA (Portaria n.º 792/98, de 22 de Setembro) |
| Inclui resíduos a produzir por projectos a implementar | Sim. | Sim | Não | Não |
| Dimensão da amostra | Não refere | Cerca de 800 industriais | Dimensão da amostra: 1995 ( 4673 empresas (taxa de resposta = 96%) 1997 ( 4502 empresas (taxa de resposta = 93%) | 3.061 mapas de empresas (1,12%) do número de estabelecimentos industriais), correspondentes a 11599 mapas de registo de resíduos |
| Classificação dos resíduos | Class. 1993 e CER | CER | CER | CER |
| Quantitativos globais dos resíduos t/ano | 1993 ( 1.365.231 (class 93) 1996 ( 2.463.494 (class 93) 1996 ( 123.915 (CER) | 108.000 (inclui resíduos não perigosos) | 1995 ( 668.062 t; 1997( 595.156 t O total de resíduos perigosos representou, aproximadamente 2,2% do total de resíduos gerados, quer em 1995, quer em 1997. | 262.875 t (1,3% do total de resíduos industriais) |
| Quantitativos de resíduos perigosos sem solução de gestão e com características para tratamento térmico (t/ano) | 16.306 | --- | 7.600 (para os mesmos códigos identificados pela TECNINVEST) | 32.220 |

Tabela A2.2- Tipologia dos resíduos perigosos.

|  | Tecninvest | INE |
| --- | --- | --- |
| Solventes orgânicos halogenados | 070103 080101 140101 070107 140102 070203 140301 070303 140302 070503 070507 070509 070603 | Não especifica |
| Solventes [orgânicos] não halogenados | 070104 080102 140103 070404 070108 140105 070204 140303 200113 070208 070304 070504 070604 070701 070704 | Não especifica |
| Ácidos/base | 110105 110106 110107 | Não especifica |
| Óleos | 130000 | 130000 |
| Soluções com metais pesados | 110103 110302 | Não especifica |
| Soluções com cianetos | 110101 110102 | Não especifica |
| Lamas inorgânicas | 060404 100506 110108 190201 060405 | Não especifica |
| Sólidos inorgânicos | 070110 100104 160403 190103 070510 190104 | Não especifica |
| Lamas orgânicas e sólidos orgânicos | 050103 070110 080102 130501 050105 070108 080107 050108 070208 080402 160700 050401 070210 160705 070408 070508 200112 070510 070608 070610 070707 070708 070710 | Não especifica |

|  | Tecninvest | INE |
| --- | --- | --- |
| Indústria extractiva |  | 130101 130201 140103 130102 130202 160601 130103 130203 130106 130601 130107 130108 |
| Indústria têxtil | --- | 040211 130101 140103 050103 130102 140201 050804 130106 140403 060101 130201 190104 060199 130202 190803 060202 130203 200121 060299 130301 070301 130305 070304 130501 070601 130502 100304 130601 |
| Indústria do couro e dos produtos do couro | --- | 040103 130106 140102 040211 130107 140103 070201 130202 140104 070204 130203 140203 200112 130403 200113 130601 |
| Indústrias de pasta, de papel e cartão e seus artigos, edição e impressão | Artes Gráficas 130000 080107 090100 Sector de pasta e papel --- | 060203 110103 140102 070203 120107 140103 070204 120109 140106 070301 120110 140405 070303 130103 160201 070304 130105 160601 080101 130106 190104 080102 130107 190201 080301 130108 200112 080302 130201 200113 080305 130202 200117 080306 130203 090101 130301 090102 130305 090103 130502 090104 130505 090105 130601 090106 |
| Fabricação de coque, produtos petrolíferos refinados e combustível nuclear | Refinarias de petróleo 050103 050105 050401 | 050103 130103 140103 050105 130107 050108 130108 050401 130202 130203 130505 130601 |
| Fabricação de artigos de borracha e de matérias plásticas | Indústria da borracha --- Fabricação de artigos de matérias plásticas --- | 060199 120106 130203 070201 120107 130305 070207 120109 130502 070210 120110 130601 080101 130101 140103 080102 130106 080106 130107 080107 130201 080301 130202 |
| Fabricação de outros produtos minerais não metálicos | Produtos minerais não metálicos --- | 030201 130101 140101 060102 130103 140103 060199 130106 160601 060201 130107 160706 061300 130201 070304 130202 080101 130203 100104 130305 100304 130601 |
| Indústrias metalúrgicas de base e de produtos metálicos (DJ) Fabricação de máquinas e de equipamento, N.E. (DK) Fabricação de material de transporte (DM) | Indústrias metalúrgicas de base --- Fabricação de produtos metálicos e de máquinas, equipamento e material de transporte 070203 110101 130000 070204 110102 140101 070303 110103 140102 070304 110105 140103 080107 110106 140301 080402 110107 140302 110108 140303 110302 190201 | 050603 110101 130203 060101 110102 130301 060102 110103 130303 060104 110105 130305 060105 110106 130501 060199 110107 130502 060201 110108 130505 060202 110202 130601 060299 110301 140101 060311 120106 140102 060402 120107 140103 060405 120108 140104 080101 120109 140105 080102 120110 140106 080106 120111 140107 080107 120112 140304 090103 120301 140405 100304 120302 160201 100307 130101 160401 100308 130103 160601 100309 130104 160602 100401 130105 160706 100402 130106 190107 100501 130107 190201 100502 130108 190803 100506 130201 200113 130202 200121 |
| Produção e distribuição de electricidade, de gás e de água | Produção de electricidade 100104 | 080102 130302 140107 100104 130303 160201 130101 130304 160601 130103 130305 160602 130106 130401 160603 130107 130502 160705 130201 130505 160706 130202 130601 170601 130203 140103 200121 130301 190803 |

Tabela A2.3- Sectores de actividade responsáveis pela produção de resíduos. Comparação das áreas indicadas pelo relatório da TECNINVEST e pelo INE

| Tecninvest | INE |
| --- | --- |
| Indústria extractiva | Extracção de produtos energéticos (CA) Indústrias extractivas com excepção da extracção de produtos energéticos (CB) |
| --- | Indústrias alimentares, das bebidas e do tabaco (DA) |
| Sector têxtil | Indústria têxtil (DB) |
| Sector dos curtumes | Indústria do couro e dos produtos do couro (DC) |
| --- | Indústrias da madeira e da cortiça e suas obras (DD) |
| Sector de pasta e papel Artes gráficas | Indústrias de pasta, de papel e cartão e seus artigos, edição e impressão (DE) |
| Refinarias de petróleo | Fabricação de coque, produtos petrolíferos refinados e combustível nuclear (DF) |
| --- | Fabricação de produtos químicos e de fibras sintéticas ou artificiais (DG) |
| Indústria da borracha Fabricação de artigos de matérias plásticas | Fabricação de artigos de borracha e de matérias plásticas (DH) |
| Produtos minerais não metálicos | Fabricação de outros produtos minerais não metálicos (DI) |
| Indústrias metalúrgicas de base Fabricação de produtos metálicos e de máquinas, equipamento e material de transporte | Indústrias metalúrgicas de base e de produtos metálicos (DJ) Fabricação de máquinas e de equipamento, N.E. (DK) Fabricação de material de transporte (DM) |
| --- | Fabricação de equipamento eléctrico e de óptica (DL) |
| --- | Indústrias transformadoras, N.E. (DN) |
| Produção de electricidade | Produção e distribuição de electricidade, de gás e de água (EE) |
| --- | Construção (FF) |
| Produtos químicos inorgânicos de base | --- |
| Produtos químicos orgânicos de base | --- |
| Fabricação de adubos | --- |
| Preparação de pesticidas | --- |
| Fabricação de resinas e fibras sintéticas | --- |
| Fabricação de tintas, vernizes e lacas | --- |
| Fabricação de produtos farmacêuticos | --- |
| Fabricação de sabões, detergentes e outros | --- |
| Fabricação de óleos e gorduras não alimentares | --- |
| Fabricação de produtos químicos diversos | --- |
| Fabricação de artigos de fibrocimento | --- |
| Comércio e serviços | --- |

Tabela A2.4- Operações de eliminação/valorização (Directiva 91/156CEE de 18 de Março de 1991).

| Código | Operações de eliminação/valorização |
| --- | --- |
| 1 | D10 - Incineração em terra D11 - Incineração em mar |
| 2 | R10 - Espalhamento no solo em benefício da agricultura ou da ecologia, incluindo compostagem |
| 3 | R09 - Utilização principal como combustível ou outro meio de produção de energia |
| 4 | D08 - Tratamento biológico não especificado noutro ponto ... que tenha como resultado compostos ou misturas eliminados por outro processo D09 - Tratamento físico-químico não especificado noutro ponto ... que tenha como resultado ... D13 - Mistura antes de uma das restantes operações de eliminação/valorização |
| 5 | D01 - Depósito à superfície D02 - Tratamento em meio terrestre D03 - Injecção em profundidade D04 - Lagunagem D05 - Depósito em aterro D06 - Descarga de resíduos sólidos em meio aquático, excepto marítimo D07 - Imersão em meio marítimo, ... D12 - Armazenamento permanente D14 - Reacondicionamento antes de uma outra operação D15 - Armazenamento antes de uma das outras operações, com exclusão do armazenamento temporário antes da recolha, no local onde esta é efectuada |
| 6 | R01 - recuperação/regeneração de solventes R02 - reciclagem ou recuperação de substâncias orgânicas não utilizadas como solventes R03 - Reciclagem ou recuperação de metais ou compostos metálicos R04 - Reciclagem ou recuperação de outras matérias inorgânicas R05 - Regeneração de ácidos ou bases R06 - Recuperação de produtos que servem para captar poluentes R07 - Recuperação de produtos provenientes de catalisadores R08 - Regeneração ou outros reempregos de óleos R11 - Utilização de resíduos obtidos a partir de uma das operações abrangidas pelos pontos R01 a R11 R12 - Ofertas de troca de resíduos para serem submetidos a qualquer das operações R01 a R11 R13 - Acumulação de materiais com excepção do armazenamento temporário antes da recolha no local onde esta é efectuada |

Tabela A2.5- Operações de eliminação/valorização.

| Códigos | Operações de eliminação/valorização |
| --- | --- |
| 1, 4 e 5 | Eliminação |
| 2,3 e 6 | Valorização |

Tabela A2.6- Tratamento final mais adequadas às diferentes categorias de resíduos

| Tratamento |  |
| --- | --- |
| Térmico | Orgânicos halogenados Solventes não halogenados Lamas orgânicas Sólidos orgânicos |
| Físico-químico | Ácidos/bases Soluções com metais pesados Solução com cianetos Outras soluções aquosas |
| Aterro | Lamas inorgânicas Sólidos inorgânicos |

ANEXO II

Cálculos de Emissões de Dioxinas/Furanos por Cimenteiras na Queima de Resíduos Industriais Perigosos e Comparação com outras Fontes de Dioxinas/Furanos

# Emissão de dioxinas/furanos por cimenteiras para a capacidade máxima de produção de cimento e com os limites máximos permitidos na UE para a emissão de dioxinas/furanos:

Limite máximo de emissões de dioxinas/furanos por cimenteiras: 0,1 ng I-TEQ/ Nm3

Volume de combustão: 2,05 Nm3/ kg  clinquer  (10% O2)

Produção de cimento para uma unidade de elevada produção como Souselas: 2 milhões toneladas de clinquer por ano

Produção total de dioxinas/furanos por ano:

2x109 kg clinquer x 2,05 Nm3/ kg clinquer x 0,1x10-9 g I-TEQ/ Nm3 = 0,41 g I-TEQ

Queima de lenha:

Emissão de dioxinas/furanos para queima de madeira em fogões de sala: 200 ng I-TEQ/ kg lenha

Uma utilização regular de um fogão de sala consome tipicamente no nosso país cerca de 4 ton/ano.

1 fogão de sala que queime 4 ton /ano produz: 200 x10-9 g I-TEQ/ kg x 4 x103 kg/ano = 8x10-4 I-TEQ g /ano.

Quantos fogões de sala equivale a emisóão anual de dioxinas/furanos  por uma cimenteira:

0,41g I-TEQ/ 8x10-4 I-TEQ g =  513 fogões

O máximo que corresponde à queima de RIP será 1/3 deste valor, cerca de 170 fogões.

Cremação de cadáveres:

Emissão de dioxinas/furanos por cadáver cremado:  4 a 28 (g I-TEQ 1

Valor médio:  16 (g I-TEQ

Quantos cadáveres correspondem à emissão de uma unidade cimenteira:

0,41 (g I-TEQ / 16x10-6 g I-TEQ  = 25600 cadáveres

O máximo que corresponde à queima de RIP será 1/3 deste valor, cerca de 8540 cadáveres cremados.

Crematório de uma cidade como Lisboa:

Procede à cremação de 2000 cadáveres por ano

Emissão de dioxinas/furanos por ano do crematório: 2000 x 16 (g I-TEQ = 0,032 g I-TEQ

Em emissões de dioxinas/furanos uma cimenteira equivale a um certo número de  crematórios:  0,41 g / 0,032 g =  13 crematórios

O máximo que corresponde à queima de RIP será 1/3 deste valor, o que equivale a cerca  de 4 crematórios.

# Emissão de dioxinas/furanos por cimenteiras na queima de RIP estimados para  co-incineração em Portugal:

Para um combustível preparado a partir de resíduos com uma capacidade calorífica média de 15MJ/kg, e dado que o processo de produção de cimento requer 3000 MJ/ton clinquer, são necessários 200 kg RIP /ton clinquer. A base dos cálculos acima apresentados foi a de uma produção anual de 2 milhões de toneladas de clinquer para os quais seriam necessários 400 000 ton de RIP. Como a nossa estimativa de RIP incineráveis não excede os 80 000 ton/ano, os números acima apresentados devem ser divididos por cinco. E se considerarmos que a co-incineração se processará em duas cimenteiras, para os efeitos locais ainda se requer uma nova divisão por 2, o que corresponde a uma emissão anual de 0,41 g I-TEQ /10 =  0,04 g I-TEQ/ano, para o limite máximo legal de emissão. Se  se considerar o valor mais realista que é a média europeia, cinco vezes menor que o limite máximo, a emissão será de 0,008 g I-TEQ/ano.

Em face destas considerações estima-se que a emissão anual de dioxinas/furanos devida à co-incineração de  RIP em Portugal (40 000 ton/ano) não exceda o efeito da emissão de dioxinas/furanos de 51 fogões de sala a queimar  4 ton/ano de lenha normal ou de  1,2 crematórios numa cidade como Lisboa.

Em suma, a emissão de dioxinas /furanos devida à queima de RIP em co-incineração por cimenteiras em Portugal não tem relevância ambiental a nível local, regional ou global.

Emissão de dioxinas/furanos por incineradoras hospitalares:

Emissão de dioxinas/furanos por tonelada de resíduos queimados em incineradoras hospitalares:  0,8 mg I-TEQ 1.

Quantidade de resíduos queimados por ano (1999) na incineradora do Hospital de Coimbra: 1770 ton/ano. Total de emissão de dioxinas/furanos: 0,8x10-3 g I-TEQ/ton x 1770 ton/ano = 1,42 g I-TEQ/ano.

Quantidade de resíduos queimados por ano (1999) na incineradora do Hospital de Leiria: 480 ton/ano. Total de emissão de dioxinas/furanos:

0,8x10-3 g I-TEQ/ton x 480 ton/ano = 0,38 g I-TEQ/ano.

A emissão de dioxinas/furanos para queima de resíduos hospitalares na incineradora do Hospital de Coimbra é cerca de 35 vezes superiores à emissão por queima de 40 000 ton RIP numa cimenteira como Souselas, estando a cimenteira a operar no limite máximo de emissão: (1,42 g I-TEQ/ano)/( 0,04 g I-TEQ/ano) = 35. Se se considerar a média de emissão europeia, a relação entre a incineradora hospitalar e a cimenteira a queimar RIP ainda é superior: (1,42 g I-TEQ/ano)/( 0,008 g I-TEQ/ano) = 177 vezes.

# LISTA DE BIBLIOGRAFIA CONSULTADA MAIS RELEVANTE

101 Facts About the Incineration of Hazardous waste at TXI's Midlothian Cement Plant. Downwinders at Risk, Texas, EUA

ACE Waste Group “About Dioxins”. http://www.ace-energy.com.au/htm/benefits/dioxine.htm

Acharya P. e Pfrommer C. (1998) “Twenty Years of Site Remediation Via Incineration in the United States” Environmental Progress, 17, nº 1, pag. 31-37

ADEME (1998) “Estude des Filières de Recyclage et de Valorization Énergique des Huiles usagées.” Rapport de Synthèse (Ecobilan - Maio 1998); Revue Critique (Bio Intelligence Service - Abril 1999)

Alexander’s Gas & Oil Connections (1998) “EPA announces tougher NOx standards for new power plants”. News and Trends, North America, Vol. 3, issue #25 - October 27. http://www.gasandoil.com/goc/news/ntn84437.htm

Allen R. e Swithenbank J. (1997) “The Incineration Paradox: Ray Allen and Jim Swithenbank Set the Scene for a Major Incineration Conference” The Chemical Engineer, pag. 22-23, Maio 8

Allen R. e Swithenbank J. (1999) “Sanity of the Bonfires.” The chemical engineer, Incineration. pag. 24-25, Maio 27

Allsopp M. (1994) “Achieving Zero Dioxin: An Emergency for Dioxin Elimination”. Greenpeace. http://adam.greenpeace.org/~toxics/reports/azd/azdtop.html

Alternativas Tecnológicas e Riscos da Incineração em incinerador. Impacto2000, cap. II,III,IV

American Lung Association. Recycling or Disposal: Hazardous Waste Combustion in Cement Kilns - V. Environmental Concerns Raised by Combustion of Hazardous Waste in Cement Kilns

American Society for Quality. http://www.asq.org/standcert/iso14.html

American Waste Group. http://www.american-waste.com/

API Thesaurus “Frequently Used Keywords in API EnCompass: Environment”. http://www.csa2.com/helpV3/apikeys.html

ATILH (1995) Valorisation des Residus dans les Fours Cimenterie. Association Technique da l’Industrie Liants Hydrauliques, Paris, França. Maio

ATL – Air Toxics Ltd. http://www.airtoxics.com/

Basel Convention: Dratf Technical Guidelines on Incineration on Land (D10). http://www.unep.ch/sbc/tech-d10.html

Basler E. (1995) Bases de la Valorisation des Combustibles de Substitution en Cimeterie. Groupe de Travail “Noveaux Combustibles pour l’Industrie Cimentière”, Maio

Berdowski J. J. M., Van der Most P. F. J. e Wessels Boer R. (1995) “Combustion in Industry: Cement.” TNO Institute of Environmental Sciences, Energy Research and Process Innovation, Holanda, Novembro. www.eea.dk/aegb/cap03/b3311.htm

Berglund R. L. e Snyder G. E.(1990) “Waste minimization: The sooner the better.” Chemtech, pag. 740-746, Dezembro

Blackman Jr W. C. (1996) “Basic Hazardous Waste Management” - Second Edition, Lewis Publishers, EUA

Booz-Allen e Hamilton Inc. “Solid Hazardous Waste Exclusions”, under contract 68-W6-0016 to EPA. http://www.epa.gov/epaoswer/hotline/training/excl.txt

Borrego C. et al. Estarreja: Sistema Integrado de Gestão de Resíduos Industriais; Unidade de Incineração e Tratamento Físico-Químico; Estudo de Impacte Ambiental: Resumo não Técnico.

Bortz S. J., Shore D. E., Garrad N., Pirkey J., Facchiano (1997) “Ultra-Low NOx Rapid Mix Burner Demonstration at Con Edison’s 59th Street Station”, Presented at the: EPRI-DOE-EPA Combined Utility Air Pollution Control Symposium, August 25 - 29, 1997. http://www.toddcombustion.com/epricond.htm.

Brammer Standard Company. http://www.brammerstandard.com/

Brenner L. P. e Stibolt T. B. (1999) “An analysis of Kriistina Iisa's Report Concerning the Emission of Dioxin and the use of PAS Carbon Filters for The Oregon Environmental Quality Commission” http://www.orcpr.org/iisaffadavit.html

Brunner C. R. (1994) “Hazardous Waste Incineration” – Second Edition, McGraw-Hill, Nova Iorque, EUA

Cadence Environmental Energy Inc. “Now, Solid Hazardous Waste can be Recycled as Energy in Cement Kilns Thanks to the Feed Fork from Cadence Environmental Energy” http://www.cadencerecycling.com/shw.html

Cadence Environmental Energy Inc. “Recycling Pharmaceutical Wastes as Energy”. http://www.cadencerecycling.com/Pharm.html

Cains P. W., McCausland L. J., Fernandes A. R. e Dyke P. (1997) “Polychlorinated Dibenzo-p-dioxins and Dibenzofurans Formation in Incineration: Effects of Fly Ash and Carbon Source.” Environmental Science Technology, vol. 31, pag 776-785

Calheiros J. M. e Conceição M. (1998) Saúde Pública: Tomo 9. Scoreco: Estudo de Impacte Ambiental do Projecto de Eliminação de Resíduos Industriais pelo Sector Cimenteiro, Março

California Energy Commission (1998) “Definitions of Terms Used In California Refining Industry Operating Reports”. http://www.energy.ca.gov/fuels/oil/refinery_output/definitions.html

Campbell Jr. C. E. (1997) “Incineration: Tested and True” Chemical Engineering, pag. 142-145, Maio

Carneiro A. P. (1979) “Poluição Atmosférica na Indústria do Cimento” Serviços de Estudos do Ambiente, Secretaria de Estado do Ordenamento Físico, Recursos Hídricos e Ambiente, Fevereiro

Carroll G. J., Thurman R. C. e Fournier Jr. D. J. (1995) “Mercury Emissions from Hazardous Waste Incinerator Equipped with a State-of-the-Art Wet Scrubber.” Journal of the Air & Waste Management Association, vol. 4, pag. 730-736, Setembro

Carvalheira P., Gois J. e Ribeiro J.(1999) “A co-incineração de resíduos industriais na indústria cimenteira.” Tecnohospital, nº2, Março

Castle Cement (1990) Cement Manufacture and Associated Processes. Castle Cement Ltd.

Castle Cement (1995) Inspectorate of Pollution; Commentary on BPEO Report and Associated Tests on Kiln at Ribblesdale Works. Castle Cement Ltd., Janeiro 24

CATOR (1998) CATOR: Gestion Integral de los Aceites Usados, Madrid, Espanha. Junho 4

CCC Research Groups: Cement Science and Aggregate Studies. http://www.sheffield.ac.uk/uni/academic/A-C/ccc/groups/cemsci.html

CDC- Centers for Disease Control and Prevencion “NIOSH Pocket Guide to Chemical Hazards-Appendices”. http://www.cdc.gov/niosh/npg/nengapdx.html

Cembureau (1997) “Workshop on Co-Incineration of Waste”. The European Cement Industry. Organizado pela Comissão Europeia, Belgirate (Itália), Outubro 9-10. http://www.eeb.org/activities/coincincement.htm

Cembureau (1999) “ Environmental Benefits of Using Alternative Fuels in Cement Production”. A Life-Cycle Approach. Cembureau - The European Cement Association, Bruxelas, Bélgica. Fevereiro

Cembureau. “Alternative Fuels in Cement Manufacture”. Technical and Environment Review

Cement Forum “Cementing the Cement World”. http://www.cementforum.com/index.htm

Cement Kiln Recycling Coalition(1995) Toxic and Hazardous Waste in Cement Kilns - The Real Story; Myths and facts about protecting human health and the environment: The real story about burning hazardous waste in cement kilns. Em Protecting Human Health and the Environment, Setembro

Central de Valorização Energética da Maia. Funcionamento da Central de Valorização Energética da Maia

Cha D. K.,Sarr D., Chiu P. C. e Kim D. W. (1998) “Hazardous waste treatment technologies.” Water Environmental Research, vol. 70, nº 4, pag. 705-720

Chadbourne J. F.. “Cement kilns.” Standard Hanbook of Hazardous waste treatmnet and Disposal.

Chapter 5 - Control of Open Burning and Incineration, amended April 23, 1992. http://www.ci.huntsville.al.us/NatRes/chap5.htm - 5.2

CLP – Combined Landfill Projects “Power Generation from Landfill Gas”. http://www.clp-energy.com/

Commitment to waste disposal-Amount of industrial wastes disposed of by landfill. http://www.tepco.co.jp/plant-sit-env/environment/98report-e/indi_waste_1-e.html

Commonwealth of Pennsylvania (1997) “Proposed State Plan for Municipal Solid Waste (MSW) Landfills” Department of Environmental Protection, Bureau of Air Quality, April 22, 1997 http://www.dep.state.pa.us/dep/subject/draft_policies/emis_lan.htm

Conselho da União Europeia (1994) Directiva 94/67/CE do Concelho de 16 de Dezembro de 1994, relativa à incineração de resíduos perigosos, Documento 394L0067. Jornal oficial no. L 365 de 31/12/1994 P. 0034-0045. Eur-Lex, Dezembro 16

Conselho da União Europeia (1996) Directiva 96/61/CE do Concelho de 24 de Setembro 1996 relativa à prevenção e controlo integrados da poluição; Documento 396L0061. EUR-Lex,. Jornal oficial no. L 257 de 10/10/1996 P. 0026-0040, Setembro 24. http://europa.eu.int/er-lex/pt/lif/dat/1996/pt_396L0061.html

Constans D. L. (1994) “Burning Waste in Cement Kilns in the UK; A Comparison of Regulations in the UK versus the US EPA Regulations.” Gossman Consulting, Inc., Georgia, EUA Abril. http://www.gcisolutions.com/burnuk.htm

Constans D. L. e Gossman D. (1997) “Tire Derived Fuel Use in Cement Kilns.” GCI TECH NOTES, Gossman Consulting, Inc., Georgia, EUA. Setembro

Constans D. L.. “Sources of PCDDs/PCDFs in Cement Kiln Emissions.” Gossman Consulting, Inc., Georgia, EUA.

Consultancy Services (1994) BPEO Assessment of the Burning Cemfuel at the Ribblesdale Works of Castle Cement Limited; AEA Technology. Castle Cement Ltd., Dezembro

Cooney C. M. (1999) “Researchers Point to Incinerator Emissions as a Major Source of Atmospheric Lead Concentrations” Environmental Science & Technology, News, pag. 106A-114A

Costner P., Luscombe D. e Simpson M. (1998) “Technical Criteria for the Destruction of Stockpiled Persistent Organic Pollutants” Third Meeting of the Intersessional Group Intergovernmental Forum on Chemical Safety. Greenpeace International Science Unit, Greenpeace Austrália e Greenpeace Canadá. Yokohama, Japão

Crummett W. (1990) “Dioxin: Molecule or Poltergeist?” Chemtech, pag. 526, Setembro

Cudahy J. J. e Rigo H. G. (1998) “National Annual Dioxin Emissions Estimates for Hazardous waste incinerators.” Journal of the Air and Waste Management Association, vol. 48, pag. 1107-1111, Novembro

DDR – Daily Regulatory Reporter (1999) “Gore Introduces Revolutionary Technology to Safely, Simply Destroy Dioxins and Furans”. Sept. 22 http://www.dakotacg.com/releases/pa/sep99/bz0923a.htm

Decreto-Lei Nº 88/91, de 23 de Fevereiro. Regula a actividade da armazenagem, recolha e queima de óleos usados. Diário da República.

Degré J. P. (1996) “Waste Co-processing in Industry. Criteria’s for an optimal waste management in the Cement Industry” Holderbank, Corporate Industrial Ecology, Documento Interno

Department of Civil and Environmental Engineering “Clinker Structure”. University of Illinois. http://www.cee.ce.uiuc.edu/lange/micro/clinkstr.html

Direcção Geral do Ambiente. http://www.dga.min-amb.pt/arvore.html

Directiva 1999/31/CE do Conselho, de 26 de Abril de 1999, relativa à deposição de resíduos em aterros. Eur-Lex, Jornal Oficial L 168 de 02.07.94 http://europa.eu.int/eur-lex/pt/lif/dat/1999/pt_399L0031.html

Directiva 1999/31/CE do Conselho, de 26 de Abril de 1999, relativa à deposição de resíduos em aterros. Eur-Lex Documento 399L0031, Jornal oficial no. L 182 de 16/07/1999 P. 0001 – 0019 http://europa.eu.int/eur-lex/pt/lif/dat/1999/pt_399L0031.html

Directiva 94/31/CE do Conselho de 27 de Junho de 1994 que altera a Directiva 91/689/CEE relativa aos resíduos perigosos. http://europa.eu.int/scadplus/leg/pt/mne/m94_31.htm

Directiva 99/31/CE do Conselho, de 26 de Abril de 1999 relativa à deposição de resíduos em aterro “Gestão de Resíduos-Deposição de resíduos em aterro”. http://europa.eu.int/scadplus/leg/pt/lvb/l21208.htm

Douglas B. D. e Merril D. T. (1991) “Control of Water Quality Deterioration Caused by Corrosion of Cement-Mortar Pipe Linings“ AWWA Research Foundation, Dezembro. www.awwarf.com/exsums/90592.htm

Ducon Environmental Systems Inc. “Air Pollution Control Systems“,http://www5.thomasregister.com/ss/.1714648279/catfrm.cgi?&index=Product&search=cyclone&seq=2&pn=0035252&state=&pdm=&footer=Catalog

Eckert Jr. J. O. e. Guo Q. (1997) “Heavy Metals in Cement and Cement Kiln Dust from Kilns Co-fired with Hazardous Waste-Derived Fuel: Application of EPA Leaching and Acid-Digestion Procedures” Journal of Hazardous Materials, vol. 59 (1998), pag. 55-93

Ecosaúde (1998) Análise Psicossocial: Tomo 8. Em Scoreco: Estudo de Impacte Ambiental do Projecto de Eliminação de Resíduos Industriais pelo Sector Cimenteiro, Março

Environment Agency (1990) Consultation Paper - Substitute Fuels protocol for use on cement and lime kilns: Environment Protection Act.

Environment Agency (1998) Agency Consultants Over Protocol Over the Use of Substitute Fuels. Em www.environment-agency.gov.uk. Londres, Reino Unido. Janeiro 29

Environmental News: Environmental Block PCB Incineration (1996). Chemical Engineering, Newsbriefs, pag. 54, Maio

Environmental Research Foundation “The Basics of Landfills: How They are Constructed and Why They Fail”. http://www.zerowasteamerica.org/BasicsOfLandfills.htm

Environmental Research Foundation “The basics of landfills”. http://www.zerowasteamerica.org/LandfillDiagram.htm

Environmental Resource Center (1996) “Hazardous Waste Management Compliance Handbook” - Second Edition, editado por B. Karnofsky, Van Nostrand Reinhold, Nova Iorque, EUA

EPG (1998) “Sources of furans and dioxins in Australia: Air emissions”. Environment Australia´s Environment Protection Group (EPG). Commonwealth of Australia, Report 432b

Eratech “Summary of Regulations Affecting Cement Kilns Using Hazardous Waste-Derived Fuels in the United States”. http://www.eratech.com/papers/us_regs.htm

ERG (1998) Report of the Meeting to Peer Review “ The Inventory of Sources of Dioxins in the United States”. Final Report. EPA Contract 68-D5-0028. Eastern Res. Group Inc.

ERGO (1996) “Emission Measurements on Cement Plants in Portugal of Dioxin/Furans, Heavy Metals, Hydrogene Chloride, Hydrogen Fluoride, Sulphur Dioxide and Total Organic Carbon (TOC).” ERGO Forschungsgesellschaft mbH, Alemanha

ESHO – Environmental Health & Safety Online. http://www.ehso.com/RSSGuide.htm

Estarreja: Sistema Integrado de Gestão de Resíduos Industriais; Unidade de Incineração e Tratamento Físico-Químico; Estudo de Impacte Ambiental: Volume I

Estarreja: Sistema Integrado de Gestão de Resíduos Industriais; Unidade de Incineração e Tratamento Físico-Químico; Estudo de Impacte Ambiental: Volume II.

Eurits (1996) ”Methodology for the Determination of Technical Co-Incineration Criteria”, Eurits Publication. Fevereiro. www.eurits,org

Eurits. “The Incineration of Hazardous Waste. How to Achieve High Environmental Protection in a Free Market Contents” Eurits Publication. Fevereiro. www.eurits,org

Farag I. H. (1993) “Simulating Hazardous Waste Incineration”. The Chemical Engineer, Rotary Kiln Modelling, Março 11, 1993, pag. s11-s16

Federal Register (1995) TSCA Section 21 Petition; Response to Citizens' Petition. Federal Register, vol. 60, nº 147 [Notices], Agosto 1

Federal Register (1997) “Hazardous Waste Management System; Identification and Listing ofHazardous Waste; Petroleum Refining Process Wastes; and Land Disposal Restrictions for Newly Hazardous Wastes; Notice of Data Availability”, Federal Register 40 CFR Part 261, U. S. Environmental Protection Agency. http://www.epa.gov/docs/fedrgstr/EPA-WASTE/1997/April/Day-08/f8816.htm

Federal Register (1999a) National Emission Standards for Hazardous Air Pollutants for Source Categories; Portland Cement Manufacturing Industry: Federal Register, 40CFR Part 63, Vol 64 Nº 113, pag 31898-31962, Junho 14. EUA.

Federal Register (1999b) NESHAPS: Final Standards for Hazardous Air Pollutants for Hazardous Waste Combustors; Final Rule. Federal Register, 40CFR Part 60, et al, Vol 64 Nº 189, pag 52828-53077, Setembro 30

Felten E. (1990) “Risk? What risk?” Chemtech, pag. 330-332, Junho

Filtration & Separation (1999) “World Buyers’ Guide and Directory 1999-2000”. Filtration+Separation, vol. 36, No. 7, Setembro 1999, INDA, Reino Unido

FIRST-Foundry Industry Recycling Starts Today. http://www.foundryrecycling.org/

Fleischer O., Wichmann H. e Lorenz W. (1998) “Release of Polychlorinated Dibenzo-p-Dioxins and Dibenzofurans by Setting Off Fireworks.” Chemosphere, vol. 39, Nº 6, pag. 925-932, Junho 18. http://www.tu-bs.de/institute/oekochem/oekochem.html

Forgey J. “Volatility and Recirculation of Metals in Chlorine in Cement Kilns”, Eratech. http://www.eratech.com/papers/volatility.htm

Forgey J. “Waste-Derived Fuel use in Cement Kilns”, Eratech, Environmental Limited. http://www.eratech.com/papers/wdf.htm

Frutuoso A., Vasconcelos J. E Escaleira R. (1996) “Tratamentos Avançados“. Processos de Tratamento de Águas Residuais. ESB – Escola Superior de Biotecnologia, Universidade Catóçica Portuguesa. http://www.esb.ucp.pt/biblio/diogo/sbadv_p.html

Gasification and Coke Production http://www.ems.psu.edu/~mathews/www/lecture16.html

German Cement Industry (1996) Concrete: Hard as a rock, Strong on performance, Fair to the environment. German Cement works’ Association Research Institute of the Cement Industry. Dusseldorf, Alemanha

Gibb Environmental (1994) Inspectorate of Pollution; Emissions Survey. Castle Cement Ltd., Novembro

Gossman D (1992) “Petroleum and Petrochemical Waste Reuse in Cement Kilns”, Gossman Consulting, Inc., Published in Environmental Progress (vol. 11, No. 1) February. http://www.gcisolutions.com/P&PINCK.htm

Gossman D. (1999) “Restricting Highly Toxic Wastes at Hazardous Waste Fuels Facilities” Gossman Consulting, Inc., Georgia, EUA. GCI TECH NOTES, Vol. 5, Nº 03, Março

Goumans J. J. J. M., van der Sloot H. A. e Aalbers Th. G. (1994) Studies in Environmental Science 60, “Environmental Aspects of Construction with Waste Materials”. Elsevier, Amesterdão, Holanda

Greenpeace. “Hazardous Waste Trial Burn at Ohio Cement Kiln Demonstrate Major Toxic Emissions.” Greenpeace Fact Sheet, São Francisco, CA, EUA

Guo Q. e Eckert Jr. J. O.(1996) “Heavy Metal Outputs from a Cement kiln Co-fired with Hazardous Waste Fuels” Journal of Hazardous Materials, vol. 51, pág. 47-65, Fevereiro 1

Harnly M., Stephens R., Mclaughlin C., Marcotte J., Petreas M. e Goldman L. (1995) “Polychlorinated Dibenzo-p-dioxin and Dibenzofuran Contamination at Metal Recovery Facilities, Open Burn Sites, and a Railroad Car Incineration Facility” Environmental Science Technology, vol. 29, pag. 677-684

Heger H. J., Zimmermann R., Dorfner R., Beckmann M., Griebel H., Ketrrup A. e Boesl U. (1999) “On-line Emission Analysis of Polycyclic Aromatic Hydrocarbons down to pptv Concentration Levels in the Flue Gas of an Incineration Pilot Plant with a Mobile Resonance-Enhanced Multiphoton Ionization Time-of-Flight Mass Spectrometer” Analytical Chemistry, vol. 71, pag. 46-57

Hester R. E. e Harrison R. M. (1995) “Issues in Environmental Science and Technology: 2 - Waste Incineration and the Environment”. The Royal Society of Chemistry, Cambridge, Reino Unido

Hester R. E. e Harrison R. M. (1995) “Issues in Environmental Science and Technology: 3 - Waste Treatment and Disposal”. The Royal Society of Chemistry, Cambridge, Reino Unido

Hester R. E. e Harrison R. M. (1995) “Issues in Environmental Science and Technology:4 - Volatile Organic Compounds in the Atmosphere”. The Royal Society of Chemistry, Cambridge, Reino Unido

Ho W., Booty M. R., Magee R. S. e Bozzelli J. W. (1995) “Analysis and Optimisation of Chlorocarbon Incineration Through Use of a Detailed Reaction Mechanism.” Ind. Eng. Chem. Res. 1995, vol. 34, pag. 4185-4192

Huang S. J. (1995) “Polymer Waste Management - Biodegradation, Incineration, and Recycling.” J.M.S.-Pure Appl. Chem., A32(4), pag. 593-597

Hunsinger H., Kreisz S. e Vogg H. (1997) “Formation of Chlorinated Aromatic Compounds in the Raw Gas of Waste Incineration Plants.” Chemosphere, vol. 34 , Nos 5-7, pag. 1033-1043

I.N.E. (1999) “Estatísticas do Ambiente - Resíduos Industriais 1995 e 1997”, Informação à Comunicação Social; Resultados Definitivos; Inquérito aos Resíduos Industriais, Outubro 19 http://www.ine.pt/prodserv/destaque/d991019-2/d991019-2.html,

IMPACTO2000 (1998) Fábricas de Cimento - Anexos Técnicos: Tomo 7. Scoreco: Estudo de Impacte Ambiental do Projecto de Tratamento de Resíduos Industriais pelo Sector Cimenteiro, Julho

Impacto2000 “Estudo de Impacte Ambiental.” Impacto2000: Estado Actual do Ambiente, cap.V

Impacto2000, Canelas L. e Amorim P. (1998) Fábricas de Cimento; Relatório: Tomo 6. Scoreco: Estudo de Impacte Ambiental do Projecto de Eliminação de Resíduos Industriais pelo Sector Cimenteiro, Julho

Incinerator Design and Operation, April 23, 1992. http://www.ci.huntsville.al.us/NatRes/chap5.htm - 5.2

Instituto Português da Qualidade. http://www.ipq.pt/

Intergovernmental Forum on Chemical Safety (1996) “Persistent Organic Pollutants: Considerations for Global Action”, IFCS Experts Meeting on POPs: Final Report, Manila, Filipinas, 17-19 June 1996. http://www.chem.unep.ch/pops/indxhtms/manexprr.html

IPAMB – Instituto de promoção Ambiental “Estudos de Impacte Ambiental”. http://www.ipamb.pt/estudos2.html

IPPC (2000) Reference Document on Best Available Techniques in the Cement and Lime Manufacturing Industries. Integrated Pollution Prevention an Control. Institute for Prospective Technological Studies, European Commission, Sevilha, Espanha. Março.

ISO 14000. http://www.iso14000.com/

Jain V. K. (1993) “Supercritical Fluids Tackle Hazardous Wastes” Environ. Sci. Technol., vol. 27, No. 5, pag. 806-808

Jensen A. A. (1997) Working Document: Dioxins - Sources, Levels and Exposures in Denmark. Danish Environmental Protection. Outubro 20

Johnson J. (1996) “Study finds no correlation between chlorine incineration and dioxin formation.” Environmental Science & Technolog, vol. 30, nº 3, pag. 112A-113A

Johnson S. K., Houk L. L., Feng J., Houk R. S. e Johnson D. C. (1999) “Electrochemical Incineration of 4-Chlorophenol and the Identification of Products and Intermediates by Mass Spectrometry.” Environmental Science Technology, vol. 33, pag. 2638-2644

Kasshireninov O. E. e Fontijn A. (1998) “Modelling of Chromium Combustion in Incineration: Thermochemistry of Cr-C-H-Cl Combustion in air and selection of Key Reactions” Combustion and Flame, 113: 498-506

Khan M. R. e Reynolds J. G. (1996) “Formulating a response to the clean air Act: Phase II of the act will require additional changes in refining operations but will allow refineries to use models to predict emission performance.” Chemtech, pag. 56-61, Junho

Klabunde K.. “Nanoscale Particles Destroy Toxic Substances” Kansas State University, EUA

Knapp D. (1996) “Typical Constituents and Compounds Found in Landfill Gas”. Berkley, Ca, EUA. http://www.zerowasteamerica.org/LandfillGas.htm

Knezevicr A. e Sober M. “Treatment of Medical Waste in Bosnia and Herzegovina”. UNEP. http://www.chem.unep.ch/pops/POPs_Inc/proceedings/slovenia/KNEZEVIC.html

Krebs W., Brombacher C., Bosshard P. P., Bachofen R. e Brandl H. (1997) “Microbial recovery of metals from solids” Fems Microbiology Reviews, vol. 20, issue:3-4, pag. 605-617. Zurique, Suíça, Julho

La prévention et la Gestion des Déchets en Région de Bruxelles – Capitale – Le Plan 1998-2002. Chapitre 7: Les installations de Traitement

Lacava P.T., Pimenta A. P., Veras C. A. G. e Carvalho Jr. J. A. (1999) “Theoretical Analysis of Aqueous Residues Incineration with Oxygen Enriched Flames” Int. Comm. Heat Mass Transfer, vol. 26, Nº 7, pag. 1029-1040

LaGrega M. D., Buckingham P. L. e Evans J. C. (1994) “Hazardous Waste Management”. Capítulo11, McGraw-Hill, Nova Iorque, EUA

Lambe A. (1997) “Aterros sanitários-Parte I - Introdução”, da Acção Ambiental para O Barlavento. http://www.terravista.pt/nazare/1321/aterro1.htm

Lambe A. (1997) “Aterros sanitários-Secção II – O Subsolo”, da Acção Ambiental para O Barlavento. http://www.terravista.pt/nazare/1321/aterro2.htm

Lambe A. (1997) “Aterros sanitários-Secção III - A Atmosfera”, da Acção Ambiental para O Barlavento. http://www.terravista.pt/nazare/1321/aterro3.htm

Landfill Emissions and Energy Utilization. http://www.pechan.com/About_Us/Qualifications/Landfill_Emissions_and_Energy_/landfill_emissions_and_energy_.html

Landfills: Hazardous to the Environment, Zero Waste America Promotes the Elimination of Waste & Pollution. http://www.zerowasteamerica.org/Landfills.htm

Lehman M., Ostrowski E., Rochow G. e Dyke R. V. “The Correlation Between Heavy Metals and Dioxin Emissions In A Municipal Waste Incinerator”. http://bigmac.civil.mtu.edu/public_html/classes/ce459/projects/t11/r11.html,

Leonardo Academy Inc. “Introduction to U.S. EPA Call for State Implementation Plans (SIPs) to Reduce Nitrogen Oxide (NOx) Emissions”. http://www.leonardoacademy.org/NOx/introduction.htm

Linak W. P. e Wendt J. O. L. (1993) “Toxic Metal Emissions from Incineration: Mechanisms and Control” Prog. Energy Combust. Sci., vol. 19, pag. 145-185

Liste des Publications Diponibles a L'IBGE (1998), Bruxelas, Bélgica. Outubro

Lohse J. e Wulf-Schnabel J. (1996) “Expertise on the Environmental Risks Associated with the Co-Incineration of Wastes in the Cement Kiln "Four E" of CBR Usine de Lixhe, Belgium” Okopol, para Greenpeace Holanda, Novembro. http://www.oekopol.de/Archiv/Anlagen/CBRBelgien.htm

Lopes C. e Gonçalves R. (1998) “Emissões atmosféricas na indústria do cimento (excerto): situação portuguesa.” DGQA-SAR-1989

M. O'Connell (1997) “Gone to Blazes... Burning Hazardous Waste in Cement Kilns.” Friends of the Earth, Ltd. Briefings, Londres, Reino Unido. Abril. http://www.foe.co.uk/pubsinfo/briefings/html/19971215145335.html

Marinshaw R. e Wallace D. (1994) Emission Factor Documentation for AP-42; Section 11.6: Portland Cement Manufactoring; Final Report. Aprovado por Midwest Research Institute (MRI), para US Environmental Protection Agency, Maio 18

Marion A. M., Lanève M. D. e Grauw A. D. (1999) Comportement à la lexiviation des bétons de route: "De la teneur totale, … à la fraction lixiviée". Quatrième rapport d’avancement : CBR-Obourg; Cinquième rapport d’avancement : CCB (Rapport commun aux trois cimentiers), Dezembro

Mascolo G., Spninosa L., Lotito V., Mininni G. e Bagnuolo G. (1997) Lab-scale evaluations on formation of products incomplete combustion in hazardous waste incineration: influence of process variables. Water Science Technology, vol. 36, nº 11, pag. 219-226

Materialen (1997) Identification of Relevant Industrial; Sources of Dioxins and Furans in Europe (The European Dioxin Inventory) Final Report

Maynard A. W. (1990) “Environmental Tests: Are they valid?” Chemtech, pag.151, Março

McCrady J. K. e Maggard S. P. (1993) “Uptake and Photodegradation of 2,3,7,8-tetrachlorodibenzo-p-dioxin Sorbed to Grass Foliage” Environmental Science Technology, vol. 37, pag. 343-350

McCulloch A., Aucott M. L., Benkovitz C. M., Graedel T. E., Kleiman G., Midgley P. M. e Li Y.-F. (1999) “Global Emissions of Hydrogen Chloride and Chloromethane from Coal Combustion, Incineration and Industrial Activities: Reactive Chlorine Emissions Inventory” Journal of Geophysical Research, vol. 104, nº D7, pag. 8391-8403, Abril 20

McDermott International, Inc. http://www.mtiresearch.com/expernce.html - Demonstration%20of%20Coal%20Reburn

Ministério de Ambiente (1998) Parecer da Comissão de Avaliação de Impacte Ambiental: Projectos de Eliminação de Resíduos Industriais pelo Sector Cimenteiro, Dezembro

Ministério do Ambiente, IDAD, Instituto da água e Pinheiro M.. Projecto de Eliminação de Resíduos Industriais pelo Sector Cimenteiro

Ministérios da Indústria e Energia e do Ambiente e Recursos Naturais (1993) Legislação Nacional, Anexos: Portaria nº 286/93 de 12 de Março. http://www.diramb.gov.pt/data/basedoc/TXT_LN_401_2_0001.htm

Mobbs P. (1998) “Toxic Emissions from Landfill”, Extracts from Claire Robinson's evidence to the appeal Inquiry, July 1998. http://www.gn.apc.org/pmhp/arrow/toxics.htm

Montague P. (1987) “EPA Says all Landfills Leak, even those Using Best Available Liners”, Rachel’s Environment & Health Weekly #37, August 10. http://www.monitor.net/rachel/r37.html

Montague P. (1987) “Recycling is Hampered; it Can’t compete With Low Cost Landfills”, Rachel’s Environment & Health Weekly #29, June 15. http://www.monitor.net/rachel/r29.html

Montague P. (1988) “Decade-Old Study Revealed the Polluting Effects of Landfills”, Rachel’s Environment & Health Weekly #71, April 4. http://www.monitor.net/rachel/r71.html

Montague P. (1988) “Leachate from Municipal Dumps has some Toxicity as Leachate from Hazardous Waste Dumps”, Rachel’s Environment & Health Weekly #90, August 15. http://www.monitor.net/rachel/r90.html

Montague P. (1989) “Analyzing Why all Landfills Leak”, Rachel’s Environment & Health Weekly #116, February 14. http://www.monitor.net/rachel/r116.html

Montague P. (1990) “#174: Hazardous Waste Incineration in Cement Kilns: 'Recycler's' Paradise” RACHEL'S Environment & Health Weekly, Environmental Research Foundation, Março 28. http://www.monitor.net/rachel/r174.html

Montague P. (1991) “New Tactics to Drive Toxics Out of Cement Kilns” RACHEL'S Environment & Health Weekly, Environmental Research Foundation, Julho 24. http://www.monitor.net/rachel/r243.html

Montague P. (1991) “Toxic Gases Emitted from Landfills”, RACHEL'S Environment & Health Weekly #226, March 27, 1991. http://www.monitor.net/rachel/r226.html

Montague P.(1992) “Cement and Kiln Dust Contains Dioxins” RACHEL'S Environment & Health Weekly, Environmental Research Foundation, Dezembro 2. http://www.monitor.net/rachel/r314.html

MPCA (1999) “Closed Landfill Program-Insurance Recovery Effort“. Minnesota, EUA. http://www.pca.state.mn.us/cleanup/landfill-closed.html#current

Não lixem Coimbra, 19/02/1999. http://www.it.uc.pt/~emanuel/coimbra/toxicos_com_valor_energetico.html

Nelson K. (1990) “Reduce waste, increase profits.” Chemtech, pag. 476-482, Agosto

Newsome G. e Showalter B. (1996) “Hazardous Waste Landfills”. Groundwater Pollution Primer. http://www.ce.vt.edu/enviro2/gwprimer/hazmat/hazmat.html

Niessen W. R. (1995) “Combustion and Incineration Processes; Applications in Environmental Engineering” - Second Edition, Revised and Expanded, Marcel Dekker, Nova Iorque, EUA

NIRO, Inc. “Niro High Temperature Fluidized Bed Incineration”. http://www.enquip.com/NIRO.htm

OBORG. La Valorization de Résidus par Obourg: une Contribuition à la Protection de l’Environment et au Développement Durable

Operating Plan for the Landfill Bioreactor Project at the New River Regional Landfill, March 23, 1999. http://www.bioreactor.org/Bioreactor_Operations_Plan.htm

Paramount Pollution Control Ltd. http://www.paramountpollution.com/

Park B.-I., Bozzelli J. W. e Booty M. R. (1997) “Polymer Pyrolysis and Oxidation Studies in a Continuous Feed and Flow Reactor: Cellulose and Polystyrene.” Environmental Science Technology, vol. 33, pag. 2584-2592

Pehlivan M., Pehlivan E. e Kara H. (1994) “Analysis of Polychlorinated Dibenzofurans (PCDF's) in Fly Ash from Waste Incineration Plant” Journal of Analytical Toxicology, vol. 18, pag. 397-401, Novembro

Pennsylvania's Department of Environmental Protection “Household Hazardous Waste”. http://www.dep.state.pa.us/dep/deputate/airwaste/wm/HHW/HHW.htm

Pinheiro Z. (1998) “Lixos Tóxicos Duplicam” - As 33 mil toneladas anuais já são suficientes para viabilizar economicamente a exploração de uma incineradora dedicada. Em “O Independente”, Dezembro 10

Pollution Online “Carbon adsorber”. http://www.pollutiononline.com/Content/ProductShowcase/product.asp?DocID={AA82448F-EDE7-11D2-94BD-00A0C9B3BDF2}&VNETCOOKIE=NO

Poncelet E. (1994) “ Incinerations des Dechets en Cimenterie: Evaluation des Performances”. ADEME - Agence de L'Invironnement et de la Maîtrise de L’Énergie. Documento Confidencial.

Power Generation Technology AAEC (Advanced Alternative Energy Corp.) home page

Preguntas y Respuestas Relativas al Uso de Combustibles Procedentes de Residuos Líquidos para su Valorización en Hornos de Cementeras; La Fabricación de Cemento, Eratech Environmental Limited, ed. 1, Junho 98. http://www.eratech.com/papers/preguntas.html

Pyrotechnix (1997) Smokeless, Odorless, Incineration Systems. TMC Manufactoring, Nova Iorque, EUA. www.incineration.com/

Quercus - Associação Nacional de Conservação da Natureza. http://www.quercus.pt/

Quercus (1999) “Óleos usados: 30 Mil Toneladas poluem anualmente o Ambiente” Quercus – Associação Nacional de Preservação da Natureza, Setembro 24

Quercus (1999) Parecer da Quercus sobre o Plano Estratégico de Resíduos Industriais (Versão Preliminar). Quercus - Associação Nacional de Conservação da Natureza, Junho 15

Recycler’s World. http://www.recycle.net/

Recycler's World “Landfill Services Category”,. http://www.recycle.net/Waste/landfill/index.html

Recycling And Hazardous Waste Information. http://www.houston.tx.us/recycling/index.html

Recycling Topics, King County, Department of Natural Resources: Solid Waste Division. http://dnr.metrokc.gov/swd/resrecy/topics.htm

Regulamento de Estruturas de Suporte e Obras de Terra, Decreto-Lei nº 32/97/M, Capítulo IV Aterros e taludes Secção I Disposições gerais. http://www.imprensa.macau.gov.mo/bo/i/97/32/declei32_4.htm

Regulamento de Estruturas de Suporte e Obras de Terra, Decreto-Lei n.º 32/97/M Capítulo II, Execução de aterros, rebaixamentos, melhoramento e reforço do terreno, SECÇÃO I, Disposições gerais. http://www.imprensa.macau.gov.mo/bo/i/97/32/declei32_2.htm

Relatif aux installations spécialiseés d'incinération et aux installations de con-incinération de certains déchets industriels spéciaux, Outubro 16, 1996

Resíduos Sólidos. http://www.resol.com.br/

RIRRC – Rhode Island Resource Recovery Corporation (1999) “Landfill”. http://www.rirrc.org/complan/status3.shtml

RIRRC-Rhode Island Resource Recovery Corporation “Landfills”. http://www.rirrc.org/landfill/rescguid.shtml

Rocha I. e Vieira D. F. (1998) “ Resíduos” - Legislação - Contencioso Contra-Ordenacional - Jurisprudência. 2ª edição actualizada. Colecção Ambiente - 2, Porto Editora.

Romic Environmental Technologies Corporation. http://www.romic.com/

RULE 1150.2. CONTROL OF GASEOUS EMISSIONS FROM INACTIVE LANDFILLS October 18, 1985. http://www.arb.ca.gov/DRDB/AV/CURHTML/R1150-2.HTM

Sabak (1999) Sabak Facts, Suécia

SAEFL (1998) Waste/Air Guidelines. Disposal of Wastes in Cement Plants. Documentation Service. Swiss Agency for the Environment, Forests and Landscape, Suiça

San Luis Obispo County Air Pollution Control District (1995) “Landfill Gas Emissions”, Adopted 7/26/95. http://www.arb.ca.gov/DRDB/SLO/CURHTML/R426.HTM

Saxena S. C. e Dewan S. S. (1996) “Co-Combustion and Fluidized-Bed Incineration of Cellulose Pellets” Energy, vol. 21, No. 10, pag 889-897

Scardi P., Gualteri A. e Bellotto M. (1997) “Industrial Applications of Powder Diffraction ". International Union of Crystallography, CPD Newsletter No. 19, December 1997 http://www.iucr.org/iucr-top/comm/cpd/Newsletters/no19xmas1997/ind-app.html

Schneider M. (1998) “The Environmental Impact of Co-combustion in Cement Kilns.” Em Proceedings of the Workshop on Co-incineration, editado por Langenkamp H., pag 186-203. Joint Research Centre, European Commission, EUR 18068 EN

Schooneuboom M. H. e Olir K. (1995) “Formation of PCDD's and PCDF's from Anthracene and Chloroanthracene in a Model Fly Ash System” Environmental Science Technology, vol. 29, pag. 2005-2009

Science Server (1995) “Cement And Concrete Research”, Vol: 25, Issue: 6, August 1995.http://sciserv.ub.uni-bielefeld.de/elsevier/00088846/sz957207/

Scoreco e IMPACTO2000. Scoreco: Esclarecimentos Suplementares Solicitados pela CAIA.

Seia (1998) Estação de transferência de Estarreja: Tomo 3. Projecto de Eliminação de Resíduos Industriais pelo Sector Cimenteiro, Fevereiro

Seia (1998) Estação de transferência de Estarreja: Tomo 4. Scoreco: Estudo de Impacte Ambiental do Projecto de Eliminação de Resíduos Industriais pelo Sector Cimenteiro, Fevereiro

Seia (1998) Estação de Tratamento do Barreiro: Tomo 1. Scoreco: Estudo de Impacte Ambiental do Projecto de Tratamento de Resíduos Industriais pelo Sector Cimenteiro, Fevereiro

Seia (1998) Estação de tratamento do Barreiro: Tomo 2. Scoreco: Estudo de Impacte Ambiental do Projecto de Eliminação de Resíduos Industriais pelo Sector Cimenteiro, Fevereiro

Seia (1998) Sumário (tomos 1-9) - Resumo não técnico. Scoreco: Estudo de Impacte Ambiental do Projecto de Eliminação de Resíduos Industriais pelo Sector Cimenteiro, Julho

Seia (1998) Transporte de resíduos: Tomo 5. Scoreco: Estudo de Impacte Ambiental do Projecto de Eliminação de Resíduos Industriais pelo Sector Cimenteiro, Fevereiro

Sellers K. (1999) “Fundamentals of Hazardous Waste Site Remediation”. Lewis Publishers, EUA

Sentencia del tribunal de Justicia: «Incumplimiento de Estado - Directiva 87/101/CEE - Gestión de Aceites usados - adaptación» (1999) Setembro 9

Simmons J. R. “The Burning Question: Trash, Hazardous Waste and Incineration”, Iowa State University, Indiana, EUA. http://www.copa.org/library/reports/iowast/burning.htm

Sistema de Informação Documental sobre Direito do Ambiente – SIDDAMB. http://www.diramb.gov.pt/siddamb.htm

Solid Waste Technologies “Landfill and Recycling Equipment”. Buyer’s Guide. http://www.solidwastetech.com/swt/archives/0899/899bg_b.asp

Sources of Concerns About the Uses of Biotechnology. http://fbox.vt.edu:10021/cals/chagedor/sources.html

Tan L. K. e Liem A. J. (1997) “Effect of Hydrochloric Acid on Sampling and Analysis of Semivolatile Organic Compounds in Incineration Flue Gas. 2. Polycyclic Aromatic Hydrocarbons.” Environmental Science Technology, vol. 31, pag. 58-66

Tan L. K. e Liem A. J. (1997) “Effect of Hydrochloric Acid on Sampling and Analysis of Semivolatile Organic Compounds in Incineration Flue Gas. 3. Chlorobenzens and Polychlorinated.” Environmental Science Technology, vol. 31, pág.1785-1793

Tasher K. (1998) EEB comments on the proposal for a new directive on the incineration of waste. Janeiro 20

TECNINVEST (1997) “Sistema de Gestão de Resíduos Industriais: Actualização do Inventário de Resíduos Quantitativos“ Ministério do Ambiente, Instituto dos Resíduos. Abril

The Australian National University “Cement”. http://online.anu.edu.au/Forestry/wood/cfb/cement.html - tab3

The European Comission (2000) “Green Paper on greenhouse gas emissions trading within the European Union, COM (2000)87”. Environment – Com Documents. http://europa.eu.int/comm/environment/docum/0087_en.htm

The Pechan-Avanti Group “Landfilling”, Ogden-waste to energy, Inc. http://www.ogden.com/energy/owte/landfill.htm

Tuomisto J., Vartiainen T. e Tuomisto J. (1997) “Synopsis on Dioxins and PCB’s” KTL, National Public Health Institute, Finlândia http://www.ktl.fi/dioxin/

U.S. Department of Energy (1994) “Appendix C Summary of Cement Stabilization, Chemical Extraction, and Vitrification Treatability Studies”. DOE/EIS-0195D http://nepa.eh.doe.gov/eis/eis0195d/eis0195d_c.html

U.S. Department of Transportation, Federal Highway Administration (FHWA) (1999) “Portland Cement”. http://fhinter.fhwa.dot.gov/infrastructure/materialsgrp/cement.html

Ueno H., Iwasaki Y., Tatsuichi S. e Soufuku M. (1997) “Destruction of chlorofluorocarbons in a cement kiln.” Journal of the Air & Waste Management Association, vol. 47, pag. 1220-1223, Novembro

United Nations Industrial Development Organization (UNIDO) “Table 4 JIS specification for cement”. http://www.unido.org/ssites/env/sectors/cementtab8.html

Universidade Nova de Lisboa – UNL “Adsorção de Ácidos Carboxílicos em Carvão Activado”. Departamneto de Química, Faculdade de Ciências e Tecnologia http://www.dq.fct.unl.pt/scripts/qf/site/QF2/AulasPraticas/Protocolos/QF2_Ads.html

UPRR-Energy Glossary. http://my.uprr.com/pub/energy/energlos.shtml

USEPA (1987) “Emissions from Landfills”. U.S. Environmental Protection Agency. http://www.epa.gov/ttnnsr01/naa1/n23_21.html

USEPA (1993) EPA Authorisation Application: Ribblesdale Works. Castle Cement Ltd., Fevereiro 22

USEPA (1995) Reports: EPA: Dioxin Reassessment Review. Copa, Inc., US Environmental Protection Agency, Science Advisory Board, Maio 15-16

USEPA (1996) Draft: Technical Support Document for HWC MACT Standards: Volume II: HWC Emissions Database. US Environmental Protection Agency, Fevereiro

USEPA (1997) “EPA Headquarters' Solid Waste Assessment - December 1997”. U. S. Environmental Protection Agency. http://www.epa.gov/oaintrnt/intrnlp2/p2/swmain.htm

USEPA (1998) “Landfill Air Emissions Estimation Model”, U.S. Environmental Protection Agency, Office of Air Quality Planning and Standards. http://www.epa.gov/oar/oaqps/landfill.html

USEPA (1998) “Protocol for Conducting Environmental Compliance Audits of Hazardous Waste Generators under the Resource Conservation and Recovery Act”, U. S. Environmental Protection Agency, Office of Enforcement and Compliance Assurance. http://es.epa.gov/oeca/ccsmd/gen_pt11.html

USEPA (1998) The Inventory of Sources of Dioxins in the USA. EPA/600/P-98/002Aa. US Environmental Protection Agency.

USEPA (1999) “Acid Rain Program Emissions Data”, U.S. Environmental Protection Agency. http://www.epa.gov/acidrain/edata.html

USEPA (1999) “Highlights of Emission Measurements: Development Activities for 1998-1999”, Emission Measurement Center U. S. Environmental Protection Agency, Office of Air Quality Planning and Standards Emissions, Monitoring, and Analysis Division, March 11. http://www.stacktest.net/update 4_99.htm

USEPA (1999) Identification and Listing of Hazardous Waste: Part 261. 40 CFR Ch. 1. US Environmental Protection Agency, Janeiro 7

USEPA (1999a) Final Technical Support Document For HWC MACT Standards- Volume I - Description of Source Categories. US Environment Protection Agency

USEPA (1999b) Final Technical Suport Document for HWC MACT Standards - Volume II: Main Report. US Environment Protection Agency

USEPA (1999c) Final Technical Suport Document for HWC Standards - Volume III: Selection of MACT Standards and Technologies. US Environment Protection Agency

USEPA (1999d) Final Technical Support Document For HWC MACT Standards- Volume IV - Compliance with the HWC MACT Standards. US Environment Protection Agency

Valeriano O. C. S. e Escalera O. A. N. (1998) “Nuevo Emplazamiento del Relleno Sanitario para el Municipio de Cochabamba”. XXVI Congreso Interamericano de Ingeniería Sanitaria y Ambiental, 1°-5 de Noviembre de 1998, AIDIS - Asociación Interamericana de Ingeniería Sanitaria y Ambiental http://www.cepis.org.pe/eswww/fulltext/resisoli/nuempl/nuempl.html

Valorsul (1999) Incineração Vs Co-incineração.

Valorsul “Questões sobre o EIA da CTRSU de S. João da Talha” Valorsul - Valorização e Tratamento de Resíduos Sólidos da Área Metropolitana de Lisboa (Norte),S.A. http://www.valorsul.pt/consulta/F2.html

van der Sloot H. A. e Hoede D. (1997) “Long Term Leaching Behaviour of Cement Mortars” ECN - Netherlands Energy Research Foundation / Nº: ECN-C--97-042, Julho

van der Sloot H. A.(1999) “Comparison of the Characteristic Leaching Behaviour of Cements Using Standard (EN 196-1) Cement-Mortar and an Assessment of Their Long-Term Environmental Behaviour in Construction Products During Service Life and Recycling” Submitted to J. Cement & Concrete Research, version 16-7-1999, Julho 16

Veranth J. M., Silcox G. D. e Pershing D. W. (1997) “Numerical Modeling of the Temperature; Distribution in a commercial hazardous waste; Slagging rotary kiln.” Environmental Science & Technology, vol. 30, Nº 9, pag. 2534-2539

Verde Vida “Aterros Sanitários”. http://www.speedlink.com.br/verdevida/recicl~10.htm

Verde Vida “Incineração”. http://www.speedlink.com.br/verdevida/recicl~4.htm

Verde Vida. http://www.speedlink.com.br/verdevida/index.htm

Verhulst D., Buekens A., Spencer P. J. e Eriksson G. (1996) “Thermodynamic Behaviour of Metal Chlorides and Sulfates under the Conditions of Incineration Furnaces” Environmental Science Technology, vol. 30, pag. 50-56

Waste & Recycling Analyis & Statistics, Zero Waste America Promotes the Elimination of Waste & Pollution. http://www.zerowasteamerica.org/Statistics.htm

Waste Age. http://www.worldwastes.com/

WEM - Wheeler Environmental Management “What is Landfill Gas (LFG)?”. http://www.ch4gas.com/aboutlfg.htm

Wentz C. A. (1995) “Hazardous Waste Management” - Second Edition, McGraw-Hill, Nova Iorque, EUA

Wey M., Hwang J. H. e Chen J. C. (1996) “The Behaviour of Heavy Metal Cr, Pb and Cd During Waste incineration in Fluidized Bed Under Various Chlorine Additives” Journal of Chemical Engineering of Japan, vol. 29, nº 3, pag. 494-500

Wey M.-Y., Hwang J.-H. e Chen J.-C. (1998) “Mass and Elemental Size Distribution of Chromium, Lead and Cadmium under Various Incineration Conditions.” Journal of Chemical Engineering of Japan, vol. 31, Nº 4, pag. 506-517

What is Dioxin? (1998) Dioxin Homepage, www.enviroweb.org/enviroissues/dioxin, Dezembro 11

Wheatley L., Levendls Y. A. e Vouros P. (1993) “Exploratory Study on the Combustion and PAH Emissions of Selected Municipal Waste Plastics” Environ. Sci. Technol., vol. 27, No. 13, pag. 2885-2895

Williams P. T. (1998) “Waste Treatment and Disposal”. John Wiley & Sons, Inglaterra

Winders H.(1997) “An Evaluation of a Cement Kiln's Emissions While Under Worst Case Operating Conditions” Rock Products Conference, Gossman Consulting, Inc. http://www.gcisolutions.com/worst.htm

Woodford J. “Changes Required in Hazardous Waste Incinerator Trial Burns and Waste Analysis Plants to Fully Implement "Bif" Requirements.” Gossman Consulting, Inc., Georgia, EUA. http://gcisolutions.com/hwi_waps.htm

Yusoff N., Moy B. e Tong C. (1996) “Fluid Bed Incineration”, December 9. http://members.tripod.com/matyus/fbi-paper/

Zeevalkink J. A. (1997) “The Materials and Energy Potencial Method for the Quantitative Distinction Between Waste and Elimination in the Cement Industry” TNO-MEP-R96/502 TNO Institute of Environmental Sciences, Energy Research and Process Innovation, Maio 23

ZGO “Dump Site Expansion from 1965 to 1995”. Jakusevac – Dump Site Zagreb. http://www.zgo.hr/deponij/jakusevec-dump-site.html

# Footnotes

Working Document: Dioxin Sources, Levels and exposures in Denmark. Danish Environmental Protecion Agency, 20 Oct. 1997.